## Slide 1
Cruise control using image analysis
Group no: 3
Domain: Digital Image processing
Project Guide: dr. Subhash Kulkarni, Principal, pesu-ecc
Students:
AASHIKA CHAKRAVARTY (1PE17EC003)
ARPITH S (1PE17EC023)
CHETAN KUMAR NAVALE (1PE17EC035)
SURYARAJ MACHANI (1PE17EC144)
1

## Slide 2
ProjecT OVERVIEW AND WORK DONE
To build and program a car capable of detecting the lane and operating in real time by responding to daily traffic situations.
1.Lane Detection
The lane detection is done by passing each frame of the video taken from the camera through the following below steps:
PRE-PROCESSING AND LANE DETECTION STEPS:
1a. Conversion of RGB image into HSV. - Depending on the color of lane to be detected the threshold values are taken into consideration.
1b. Apply Gaussian Blur to smoothen the image- Kernel size of (5,5)
1c. Apply Canny Edge Detector to detect the edges with a lower threshold of 50 and upper threshold of 100.
1d. Define a function to get the region of interest in the image.Un-necessary part of image is filled with black pixels. Fillpoly() function is used in python
2

## Slide 3
WORK DONE
3
DRAWING LANE LINES
1e.We pass the cropped image into the Hough transform function which takes multiple other parameters along it,those are the rho ,theta and threshold. A threshold of 20 is taken .
1f. We draw the line based on the co-ordinates returned by the hough transform.
1g. Based on the co-ordinates received we can determine the slop of the line and determine the steering direction accordingly.

## Slide 4
4
2. Traffic Object Detection using YOLO v3 and tiny weighted YOLO
YOLO is a state of an art algorithm used to detect objects. It is trained for COCO datasets which has 90 different classes.
We will use only the classes helpful for our project.
We draw bounding boxes across the traffic object detected, with a confidence score around each object detected.
We have taken into consideration several different datasets – Raw footages from Car Cam dashboard. The threshold value for hough transform, Canny detector and the region of interest changes ,depending on the video and application.
YOLO function takes in 2 parameters that are the obj_threshold, nms_threshold.

## Slide 5
5
obj_threshold: Integer, threshold for object.
nms_threshold: Integer, threshold for box.
Time taken to compute a single frame in an video was in an average of 0.93 s, which gave us an fps of 1 using the yolo model.
Tiny weighted YOLO is used which gave an average of 0.3 s for each frame and was computationally inexpensive.(fps around 4).
Tiny weight YOLO is 442% faster than YOLO when used in GPU and has a less model size also. When run on a GPU its FPS is around 244.

## Slide 6
6
#Future work – Explain about the udacity simulator and then the Unity software.
Simulation based results- Taking images as input and producing steering angle,throttle
and speed as the output.(Behaviour cloning)